## Slide 1: Secure the Openness The operator challenge
Vlad Sorici, Architecture & Services Project Manager
DefCamp - November 10th, 2016

## Slide 2: agenda
What’s the challenge
Captive portal authentication
SIM based authentication
VoWi-Fi security
Localized Wi-Fi attacks

## Slide 3: 5 fundamental values that should guide everything we do
Simple
Open
Surprising
Dynamic
Honest
So… how can you make this secure?

## Slide 4: A hyper-connected society
Internet users spend 4.8 hours online each day on their computers and 2.1 hours online on their cell phones

## Slide 5: A hyper-connected world using Wi-Fi
Smart TVs
Smart watches
Home appliances
Music player
Scales
Video cameras
Connected cars

## Slide 6: even connected irons …used by spies
The BBC reports a Russian group has uncovered embedded Wi-Fi enabled cards inside an iron
Apparently it would attach to nearby unprotected Wi-Fi and insert a virus whose purpose is not yet known
It is great to see Wi-Fi a tool for everyone – including spies! 

## Slide 7: Wi-Fi networks are a big part of the connected world
What’s Wi-Fi?
    based on 802.11 standards
What ‘s the general expectation of Wi-Fi?
    Free
    Open
    Always working, always fast

## Slide 8: Wi-Fi networks are not as simple as we would like to think or else, everybody could do it
Orange Wi-Fi network now
    5.000 Access Points
    30.000 simultaneous clients
    273.117 monthly users
    3 TB average daily traffic
Wi-Fi Services
    Operator Wi-Fi (Public)
    Business Wi-Fi (B2B and B2B2C)
    Business Mobile Wi-Fi
    Business Retail Analytics
    VoWi-Fi – Apel Wi-Fi

## Slide 9: 1st challenge create a public Wi-Fi infrastructure secure and easy to connect
Captive portal authentication
    SSID appears as “open” to the customers
    User connects to the network and opens browser
    Redirection to a captive portal where he inputs their phone number
    An SMS will be received with the password or authentication URL

## Slide 10: 1st challenge basic authentication scheme
    Device connects to network and tries to connect to http server and the Wi-Fi controller redirect it to captive portal platform
    User authenticates on th
    e captive portal and HTTPS authentication is performed
    the captive portal will indicate the controller URL that the user will access
    After the authentication, the user has now internet access
    Device connects to network and tries to connect to http server and the Wi-Fi controller redirect it to captive portal platform
    User authenticates on the captive portal and HTTPS authentication is performed
    the captive portal will indicate the controller URL that the user will access
    The controller URL will trigger the Radius Request according to user data and the captive portal should accept the request

## Slide 11: Captive portal authentication create a public Wi-Fi infrastructure secure and easy to connect
Open & Simple
    SSID is open so client will try to connect
    Only one information requested in the captive portal, with password received instantly
    Available to both mobile and desktop devices
    Some devices will not open automatically the browser so the client might not know that they need to connect
    Requires some manual configuration from the customer
Security
    only verified customers can connect
    Traffic with captive portal might not be encrypted (+ use HTTPS on the captive portal)
    Network traffic not encrypted
    Open to AP impersonation attack to gain access to client phone number (+ use HTTPS on the captive portal but requires educated user)

## Slide 12: 2nd challenge: more open & simple and more secure What? more open & simple AND more secure ?
Open & simple
    Automate the connection process
    Use existing credentials
Secure
    Use WPA2 encryption
    Use 802.1x authentication

## Slide 13: 2nd challenge: more simple and open SIM based authentication
    EAP-SIM [RFC 4186] or EAP-AKA [RFC 4187] are authentication methods that are using the SIM credentials stored in the phone
    The user doesn’t have to introduce anything
    First time set-up where user selects the authentication method, after that, the connection is automatic, just like home
    Automatic connection from the beginning for devices supporting Passpoint technology
    The permanent identity that is used is the IMSI stored in the SIM card and Wi-Fi key is negotiated without user intervention

## Slide 14: 2nd challenge: more secure 802.1x authentication
Most secure authentication method in Wi-Fi
    802.1x encapsulates between supplicant and authenticator
    RADIUS encapsulates between supplicant and authenticator
    Each protocol that uses EAP defines a way to encapsulate EAP messages within that protocol's messages. Main EAP methods: LEAP, TLS, TTLS, SIM, AKA
    Remote Authentication Dial In User Service (RADIUS) is a networking protocol that provides centralized Authentication, Authorization, and Accounting (AAA) management for users that connect and use a network service.

## Slide 15: SIM based authentication : EAP-SIM [RFC 4186]
    802.1x: EAP-Response/Identity (IMSI)
    802.1x: EAP-Request/SIM/Start (AT_VERSION_LIST)
    802.1x : EAP-Response/SIM/Start (AT_NONCE_MT, AT_SELECTED_VERSION)
    RADIUS: <<above>> (contains also IMSI in RADIUS AVP)
    MAP: authentication triplets retrieval (works also for quintets)
    RADIUS: EAP-Request/SIM/Challenge (AT_RAND, AT_MAC)
    802.1x : <<above>>-> Device runs GSM algorithms, verifies AT_MAC and derives session key
    802.1x : EAP-Request/SIM/Challenge (AT_MAC)
    RADIUS: <<above>>
    [optional] User profile retrieval
    RADIUS: EAP-Success 12. 802.1x: EAP-Success
    Further key negotiation based on PMK

## Slide 16: SIM based authentication : EAP-AKA [RFC 4187]
    802.1x: EAP-Response/Identity (IMSI)
    RADIUS: <<above>>
    MAP: authentication quintets retrieval. Server runs AKA algorithms, generates RAND and AUTN)
    RADIUS: EAP-Request/AKA-Challenge (AT_RAND, AT_AUTN, AT_MAC)
    802.1x : <<above>>-> Device runs runs AKA algorithms verifies AUTN and MAC, derives RES and session key
    802.1x : EAP-Request/AKA/Challenge (AT_RES, AT_MAC)
    RADIUS: <<above>>: Server checks the given RES and MAC and finds them correct.|
    [optional] User profile retrieval
    RADIUS: EAP-Success 12. 802.1x: EAP-Success
    Further key negotiation based on PMK

## Slide 17: SIM based authentication how secure is it?
Basic EAP protocol is not encrypted
Currently EAP-SIM/AKA in EAPOL is unencrypted
    Thus IMSI is visible (to a passive attacker) when permanent identity used for full authentication
    SOLUTION: use Pseudonym identity (derived by
    both the Device and AAA server)
    BUT REMEMBER Smartphones will connect automatically to SIM based authentication hotspots so an active attacker might reuse Orange SSID to require full authentication ID
    SOLUTION: devices should implement the
    “conservative peer policy”, that only respond to
    requests for permanent identity when no
    pseudonym identity available

## Slide 18: VoWi-Fi what is it?
User experience
    Enable Wi-Fi calling
    Connect to a Wi-Fi network
    Logo will automatically change when Wi-Fi calling is on
    You can now call using Wi-Fi internet access

## Slide 19: VoWi-Fi what is it?
Technical facts
    SIP based calling using Operator IMS infrastructure
    Access to the IMS needs to be secure so the device will create an IPSEC tunnel to the ePDG
    IKEv2 authentication will be used encapsulating same EAP-AKA authentication
    ePDG will authenticate the user through a Diameter interface with the AAA
    After the authentication, the ePDG will create a GTPv2 tunnel inside the mobile core

## Slide 20: VoWi-Fi authentication phase
    IKE_SA_INIT_REQ (SA, DH, Nonces, [NAT detection])
    IKE_SA_INIT_RESP (SA, DH, Nonces, [NAT detection])
    IKEv2_AUTH_REQ (SA, NAI <<containg IMSI>> , APN, CNFG)
    Diameter-EAP Request (NAI, APN): EAP Response
    AAA authentication vector retrieval
    Diameter-EAP Answer: EAP-Request/AKA-Challenge (AT_RAND, AT_AUTN, AT_MAC)
    KEv2_AUTH_RESP: <<above>>
    IKEv2_AUTH_REQ: EAP-Request/AKA/Challenge (AT_RES, AT_MAC)
    Diameter-EAP Request: <<above>> Server checks the given RES and MAC and finds them correct.|
    [optional] User profile retrieval & AAA update in HSS
    Diameter-EAP Answer: EAP-Success, EAP-MSK, APN config
    KEv2_AUTH_RESP: EAP Success
Notes: Initiates connection in two phases
• IKE_SA_INIT
• Negotiate cryptographic algorithms, exchange nonces, and do
a Diffie-Hellman exchange
• IKE_AUTH
• Authenticate the previous messages, exchange identities (e.g.
IMSI), and certificates, and establish the child Security
Association(s) (SA)

## Slide 21: VoWi-Fi other facts
ePDG is selected using DNS procedure
    Thus an active attacker can make a fake free hotspot, respond to DNS requests towards a fake ePDG and get user IMSI. In VoWi-Fi service, pseudonyms are not used by the devices
    SOLUTION: Deploy certificate based aproaches like
    EAP-TTLS + EAP AKA or multiple auth exchanges
    (reco of University of Oxford presentation in Blackhat
    London)
    BUT REMBEMER IMSI information might be considered a sensible information but that information alone can’t lead to fraud or decrypting IPSEC communication
ePDG must have a strong re-authentication policy behavior
Notes: ePDG must have a strong re-authentication policy behavior ; not to delete GTP tunnel before reauthentication si completed

## Slide 22: Localized Wi-Fi attacks and other Wi-Fi infrastructure security features
Wi-Fi infrastructure can detect the existence of Rogue APs
    Rogue APs can be classified using rules like SSID, RSSI, Duration, Client Count, etc.
    Extra APs can be put in monitor mode in order to scan full time the environment for these Rogue Aps
    Containment of Rogue APs can be done especially when multiple APs are deployed in one hotspot but can have legal consequences
    Using our Location services infrastructure Rogue APs, Rogue Clients, Interferers and wIPS Attackers can be detected and localized
Notes: ePDG must have a strong re-authentication policy behavior ; not to delete GTP tunnel before reauthentication si completed

## Slide 23: Localized Wi-Fi attacks location and zone of impact
Non-WiFi Interferers
Rogue Access Point
Notes: ePDG must have a strong re-authentication policy behavior ; not to delete GTP tunnel before reauthentication si completed

## Slide 24: Other security mechanism Management Frame Protection (MFP)
Problem
Wireless management frames are not authenticated, encrypted, or signed
A common vector for exploits
Solution
Insert a signature (Message Integrity Code/MIC) into the management frames
APs can instantly identify rogue/exploited management frames
Optionally, Clients and APs use MIC to validate authenticity of management frame
Beacons
Probes
Association
Beacons
Probes
Association
Notes: ePDG must have a strong re-authentication policy behavior ; not to delete GTP tunnel before reauthentication si completed

## Slide 25: Wi-Fi network and services evolution
v
Wi-Fi GW
AAA
operator Wi-Fi
[2013]
mobile Wi-Fi core connected to 3G/4G core for a seamless wireless access experience
v
Wi-Fi AP
Wi-Fi AP
aggregation switches
CPE
client location
Orange
IP network
PE
PE
Internet access
Orange central sites
Wireless Controllers
v
managed Business Wi-Fi and Orange Wi-Fi [2012]
captive portal
AAA
Hotspot Manager for personalized access and data collection
ePDG
Wi-Fi calling
[2015]
v
Retail Business Analytics
[2014]
Wi-Fi tracking info converted into actionable business metrics
analytics engine and big data located into Orange IaaS
on premise security appliance
v
Business Internet Security [2015]
traffic filtering, application control, AV/AS, IPS/IDS, DDoS
centralized security appliance and security operation center

## Slide 26: Continue your journey with Orange Defcamp Platinum Partner
Check out Business Internet Security Threat Map
App2Own – BUG BOUNTY
    Nov 10th, from 9:00 – to Nov 10th, 19:00: on site contest, with most security features activated
    Nov 11th, from 9:00 – to Nov 11th, 16:00: on site contest, with some security features deactivated
Wi-Fi PWNED Board

## Slide 27: Thank you
Vlad Sorici
Development & Innovation Team